## Slide 1: R&D Needs and Technological Tools for Water Management in the GCC Countries
Prof. Waleed K Al-Zubari
Arabian Gulf University
waleed@agu.edu.bh

## Slide 2: Overview
Introduction
GCC Water Resources & Use
Alternative Scenarios for Water Policies
GCC Water Resources Management Strategies
  Demand Management in Agricultural
  Supply Augmentation
    Desalination
    Wastewater Treatment
Suggested Framework

## Slide 3: Introduction
Arid to extremely arid climatic conditions
  Small and irregular rainfall in space & time (<100 mm/yr)
  High evaporation rates ( >3000 mm/yr)
Generally devoid of surface water resources, depends mainly on groundwater, desalination, and reuse of TSE

## Slide 4: Cont., Introduction
Accelerated development growth since the mid 1970s
Increase in the economic base, rapid improvement in the standard of living, and high rates of development
High population growth rates (>3%)
Substantial increase in water demands
GCC Total Water Demands, Bcm
GCC Population, Millions

## Slide 5: Cont., Introduction
Scarcity of natural water resources is aggravated by high population growth
Water is becoming an increasingly scarce commodity and its availability is decreasing with time
Per Capita Available Water Share in GCC
1950-2000

## Slide 6: Cont., Introduction
If this situation continue, GCC countries will experience a series of major water problems due to:
  Escalating water demands and lack of effective conservation measures
  Continuous deterioration of groundwater resources
  Slow rates of water resources augmentation
  Modest programs for wastewater treatment in rapidly developing urban communities
  Lack of solution to the issue of population growth

## Slide 7
Groundwater
91%
Treated Wastewater
1.7%
Desalinated Water
7.2%
Industrial
Municipal
Agricultural
85.1%
13.7%
1.2%
Agricultural Policies
Population & Urbanization
Growing!
Main
Pressures
GCC Water Resources & Use

## Slide 8: Alternative Scenarios for Water Policies
Essentially 3 future policy options available
  Population Policy change (high political risk, long term impact)
  Agricultural Policy change (medium political risk, medium term impact)
  Water Policy change (lower political risk, short term impact)
  Combination of two or three of the above
Selected: Water Policies: 3 extreme scenarios
  Scenario I: Baseline Scenario (Do nothing!)
  Scenario II: Augmentation of Water Supply (continue current policies)
  Scenario III: Augmentation and Policy Remedies

## Slide 9
Proposed Policies for Scenario III
  Focusing on demand management, conservation, and protection
  Priority of water supply for domestic, agriculture, and Industry, respectively
  Rational water use & allocation
  Groundwater management and protection
  Increase water use efficiency & economic productivity
  Water pollution control and environmental protection
  Institutional reforms and capacity building
Cont., Alternative Scenarios for Water Policies

## Slide 10
GCC Future Water Balance
Baseline Scenario
Supply Augmentation
Augmentation & Policy Remedies (WDM)
Cont., Alternative Scenarios for Water Policies
DEFICIT

## Slide 11
Water Resources Management Strategies
1. Demand Management & Conservation in the Agricultural Sector
2. Supply Management & Augmentation: Desalination & Treated Wastewater

## Slide 12: Demand Management in the Agricultural Sector
Increase in Areas under Irrigation in GCC, 1965-2002
FAOSTAT, 2004
KSA (LS)
UAE (RS)
Oman (RS)
Kuwait (RS)
Qatar (RS)
Bahrain (RS)

## Slide 13
Example: Wadi Al-Sarhan, KSA
Cont., Water Management Strategies

## Slide 14: Irrigation Water Share of Total Groundwater Abstraction in the GCC, 2000
WB, 2005

## Slide 15
Agriculture is now the main groundwater consumer (85%)
Irrigation efficiencies low at 30-45%; major “real” water savings can be achieved!
Traditional irrigation practices
Lack of monitoring & tariffs for irrigation water
Low value & high water consumption crops
Urgent need to apply demand management tools
To move towards modern irrigation and agricultural techniques (e.g., soilless culture)
Cont., Water Management Strategies

## Slide 16
Desertification of Agricultural Lands due to Water degradation, Bahrain
Cont., Water Management Strategies

## Slide 17
Agricultural Sector Constraints
  Water (quantity & quality)
  Lands and Soil (limited arable lands, majority infertile)
  Climate (restrictive, high evaporation losses due to use of traditional agricultural methods)
  Low agricultural sector contribution GDP (less than 1%, and decreasing)
  Low employment of national working force (mainly unskilled foreign labor)
  Comparative advantage (heavy subsidies), free trade, and external competition
Cont., Water Management Strategies

## Slide 18
A Proposed Area of Solution
  Modern Agricultural Techniques: Soil-less Agriculture
    To over-come agricultural constraints
    To achieve sustainable agriculture (expanding)
    To create more national employment opportunities
    Increase agricultural sector contribution to the GDP
    Enhance Food Security
Cont., Water Management Strategies

## Slide 19: Modern vs. Traditional Agricultural Systems
الزراعة المحمية التقليدية السائدة بدول الخليج العربي
الزراعة المحمية المتطورة والزراعة بدون تربة
زراعة محمية
زراعة محمية
زراعة مدفئة (الشتاء) ومبردة (الصيف)
زراعة مدفئة (الشتاء) غير مبردة (الصيف)
ري بالتنقيط (مياه جوفية)
ري بالتنقيط (مياه قليلة الملوحة وبمحلول مغذي) يعاد تدويرها باستمرار
زراعة في التربة مسمدة
زراعة بدون تربة (خفان)

## Slide 20: Experimental Results
Water Cost (L/Kg): savings 74-94%
Land Productivity (kg/m2 area): increase 200-900%

## Slide 21
Vision
  Establishment of “Agri-Industrial Parks”
  Contribute to food security without endangering water security
  Help in the transformation of the agricultural sector from a marginal sector to a sustainable expanding sector
  Contribute to national economy
  Create small & medium size national projects to enhance socio-economic development

## Slide 22: Development of Desalination Capacity in GCC Countries, 1980-2000
Currently the main source of water to meet spiraling domestic water supply requirements (quantity & quality) in major cities in GCC
Used directly or blended blended with groundwater
Supply Augmentation: Desalination

## Slide 23: Desalination Capacity in the GCC Countries (43% of world total capacity)
ESCWA, 2001
Cont., Water Management Strategies

## Slide 24
Extensive installation of desalination plants, but
  Desalination Cost
    Total cost of desalination plants installed up to 2001 is US$ 21 billion (heavy burden on national budget)
    Average production cost in GCC range: US$ 1-2/m3 (compared to current US$ 0.70/m3)
    Operating life (15-25 years)
  Environmental impacts
    Marine pollution (thermal, brine, residual treatment chemicals, ..)
    Air pollution by emitted oxides (mostly using oil)
  Imported Technology: GCC still do not own the technology completely, does not add to the national economy
Cont., Water Management Strategies

## Slide 25
Reduce Desalination Cost
Increase Reliability of Desalination as a Water Resource
Increase Value Added to GCC Economy from Desalination Projects
Reduce Environmental Impact
Enhance Cooperation among GCC and Arab Countries
Goals of Desalination R&D in GCC (Bushnak, 2002)
Cont., Water Management Strategies

## Slide 26
Reducing Capital Cost of Plants / New Material
Reducing the cost of O&M and Energy Consumption
Extending the Economic Life of Plants
Increasing Value Added by Co-generation
Developing Innovative Less Costly Processes
Reducing the Cost of Desalinated Water
Cont., Water Management Strategies

## Slide 27
Localizing O&M and Plant Refurbishment
Strategic Storage of Excess Desalinated Water using ASR Techniques
Localizing Design, Fabrication and Construction of Plants
Local Manufacturing of Key Spare Parts & Components
Increasing Reliability of Desalination as a Water Resource
Cont., Water Management Strategies

## Slide 28
Qualifying Local Labor to Work in Desalination Industry
Localizing Design, Fabrication, & Construction Capabilities
Maximizing the Benefits of Co-generation
Coordinating Energy Policy with Water & Power Policy
Recovery of Rare Minerals from Desalination Brines (Li, Br, etc..)
Increasing Value Added to GCC Economy from Desalination
Cont., Water Management Strategies

## Slide 29
Driven by escalating urban water consumption
Almost all countries operating modern treatment facilities with tertiary and advanced treatment
TSE represents only about 20% of the total municipal water volumes
Wastewater discharge and health hazard problems (pollution of shallow groundwater, coastlines and marine environment, water table rise in urban centers)
  Reused TSE does not exceed 12% of the available domestic water supply, and about 60% of treated wastewater
treated
reused
Supply Augmentation: Treated Wastewater

## Slide 30
Many Constraints for reuse (Al-Zubari, 2001)
  Public Attitude
  Heavy minerals accumulation in soil
  Industrial waste discharge in domestic waste networks
  Microbial pollution (to design conventional treatment plants that complies with the requirement of the WHO Health guidelines for treated wastewater reuse)
Cont., Water Management Strategies

## Slide 31
Suggested Framework
Giving WATER a prominent place in the national and regional agendas
Adoption of proactive strategic Integrated Water Resources Planning and Management
A strong shift towards demand management, conservation, and protection
Major regional investments and cooperation in
  R&D in non-conventional water technologies (desalination and treatment technologies)
  R&D Modern Agricultural technologies

## Slide 32: Thank You!